GAD-201G Specifications

The specifications apply when the GAD-201G is powered on for at least 30 minutes under +20°C~+30°C.

| DISTORTION MEASUREMENT |
| --- |
| Range | 0.1% ~ 100% full scale in 7 ranges (auto ranging) |
| Fundamental Frequency Range | 20Hz ~ 20kHz in 3 continuous ranges with fine adjustment tuning 3 spots for 400Hz, 1kHz, 10kHz |
| Input Level | 100mVrms ~ 300Vrms |
| Automatic Level Control Range | ±10dB |
| Fundamental Rejection | > 80dB |
| Second Harmonic Accuracy | ±1dB at basic frequency 20Hz ~ 20kHz |
| Residual Distortion | < 0.03% including hum and noise |
| AC VOLTAGE MEASUREMENT |
| Range | 1mVrms to 300Vrms full scale in 12 ranges (auto-ranging) |
| Frequency Response | 20Hz ~ 200kHz ±1dB |
| Input Impedance | 100kΩ ±10%, <70pF (unbalanced) |
| Accuracy | ±3% of full scale (@ 1kHz) |
| Residual Noise | < 10uV (input short circuit) |
| Output Level | X:1Vrms, Y:500Vrms at meter full scale |
| Output Impedance | Approx. 600Ω |
| POWER SOURCE |
|  | AC 100V/120V/220V/240V ±10%, 50/60Hz |
| DIMENSIONS & WEIGHT |
|  | 310(W) × 165(H) × 300(D) mm Approx. 4.6kg |