GFC-8270H / GFC-8131H Specifications

The specifications apply when the GFC-8270H / GFC-8131H is powered on for at least 30 minutes under +20°C~+30°C.

| DISPLAY |
| --- |
|  | 8 digits with Hz, kHz, MHz, GHz, s, ms, μs, and overflow |
| GATE TIME |
|  | Variable from 10ms to 10s, or 1 period of input depending on whichever is greater |
| ACCURACY |
|  | ±(resolution ± timebase error) |
| CHANNEL A |
| Range | DC coupling: 0.01Hz ~ 120MHz AC coupling: 30Hz ~ 120MHz |
| Sensitivity | 10mV typical, 50mV maximum |
| Coupling | AC or DC, selectable |
| Filter | Low pass, selectable in or out for channel A (-3dB point, nominal 100kHz) |
| Impedance | 1MΩ // 40pF |
| Attenuator | 1/1 or 1/20dB |
| Trigger Level | -2.5VDC ~ +2.5VDC |
| Adjustment Resolution | For frequency measurement, the maximum resolution is 100nHz for 1Hz and 0.1Hz for 100MHz inputs respectively. For period measurement, the maximum resolution is 10ns for 1Hz input, and 0.1x10-15s for 100MHz inputs respectively. |
| Display Accuracy | 7 digits for 1 sec gate time 6 digits for 100ms gate time 5 digits for 10ms gate time |
| Period Range | 8ns ~ 100ns (at least 7 digits displayed per gate time) |
| CHANNEL B |
| Range | 50MHz ~ 2.7GHz for GFC-8270H 50MHz ~ 1.3GHz for GFC-8131H |
| Sensitivity | <50mVrms (10mVrms typical) for GFC-8270H <40mVrms (10mVrms typical) for GFC-8131H |
| Coupling | AC only |
| TIME BASE |
| Aging Rate | 1ppm per month |
| Temperature | 5ppm, 23°C + 5°C |
| Line Variation | 0.005ppm for + 10% variation |
| POWER SOURCE |
|  | AC 100V/120V/220V/230V ±10%, 50/60Hz |
| DIMENSIONS & WEIGHT |
|  | 230(W) × 95(H) × 280(D) mm Approx. 2.2kg |